# Lesson 13: Introduction to Cartographic Modeling

What You’ll Learn: This Lab will primarily review and apply skills from previous Labs (especially Labs 8 through 11). In particular this lab will focus on buffering, creating binary flags or indicators, dissolving, and union/intersection.

You will estimate the size of the prime ruffed grouse habitat at the Cloquet Forestry Center (CFC), Carlton County, Minnesota.

Because most is review, we will not provide step-by-step instructions as we have in previous labs.  If you have questions please first refer to earlier labs and videos.

Data: \L13, including, in UTM15, NAD83, meters coordinates:

- Cloquet_roads.shp, a roads layer

- Cloquet_streams.shp, a streams/lakes layer

- Cloquet_vegetation.shp, a vegetation layer (attribute codes are described at the end of these instructions)

- Iverson_drg.img, a digital raster graphic of a USGS 7.5 topographic

What You’ll Produce: A map of CFC with areas of with identified areas of high quality ruffed grouse habitat.

Background: Ruffed grouse is a northern game bird species that thrives in disturbed forest ecosystems. The best grouse habitat is found in a mosaic of aspen patches burned or clear-cut every 40 to 50 years. This mosaic provides a food and cover in close proximity, and refuge from predators, see http://www.dnr.state.mn.us/volunteer/novdec06/grouse.html.

Optimum ruffed grouse habitat should consider proximity to:

- Brushy areas and young aspen stands for cover and summer food. Here we’ll select aspen stands that are less than 19 to 34 years old.

- Mature aspen stands with an understory of hazel or ironwood that provide food in fall, winter and spring.  In this analysis we’ll select aspen stands older than 34 years

- Dense sapling aspen stands to provide brood cover, here stands 18 years old or younger.

- Away from areas with old tall conifers that serve as winter roosts for raptors.  In this analysis, we will select conifer stands more than 105 years old.

Note that you want areas that are near all three aspen/birch ages (this is an AND combination), and also not near tall conifers. This will involve selecting stands that meet a criterion, and buffering around these stands.  The buffers for the various criteria are then overlain to identify suitable habitat.

Use the vegetation layer to identify the Aspen and Birch Stands in the CFC (see labs 8 & 9 for methods). A table at the back of this lab contains the codes for vegetation type (C_type) and for establishment year (Origin). From the establishment year you may get age, by subtraction. Assume you are doing this in 2006, the year the data were produced.

You need to identify Aspen and Birch (select by attributes) and export these stands to a separate shapefile, naming it something like AspenBirch.shp.  Then open the AspenBirch attribute table and alternately select the young, intermediate, or old tree stands, exporting each to create three new shapefiles.

Remember; use the Select By Attributes menu from the table, and use species and/or age to select a specific set of polygons. Then, right click on the source layer in the Table of Contents window, and then left click on Data ( Export Data.  This saves your selected records as new layer.

Out of the 506 Vegetation records, 111 are Aspen or Birch. Of these:

- 30 records are Young; less than 18 year,  from 2006 through 1988

- 25 records are Intermediate; between 19-34 years, from 1987 through 1972

- 30 records are Old; 34 years and over, from 1971 to 1888

Don’t use the records with 00 values in the ORIGIN (unknown age)

After creating each AspenBirch age class layer:

- Buffer each layer at 300 meters.

- Overlay the three layers using the Union or Intersect commands to create a CoverFood layer.

Intersect is perhaps easiest for combining the three age class layers into the CoverFood layer. Check each input layer and the results after each union or intersection to verify the results are correct. Do the overlays in a serial manner, e.g., intersect the Young and Intermediate buffers, then intersect the result with the Old buffer.

You now need to subtract the areas in CoverFood that are near older conifers, potential raptor perches:

- Select those records of the Cloquet_vegetation that are White Pine, Red Pine, Jack Pine,  Scotch Pine, or White Spruce (C_Type = J or C_Type = R or C_Type = W or C_Type = D or C_Type = WS).

- Save this interim layer.

- Then select those records of the interim layer that are older than 1900 (Origin > 0 and Origin < 1901).

You should have 21 records.

- Buffer this layer at 50 meters (adjacent raptor perch area)

- Erase the adjacent raptor perches from your cover/food habitat layer, via  ArcToolbox ( Analysis ( Overlay ( Erase.  If you are using the Student Home Edition, remember you need to use a different method,  create/calculate an erase attribute; ArcToolbox-Analysis( (Union, then Start Editing (Select by Attributes( delete, as described in Lab 9.

Summarize the result to estimate the total size of the potential grouse habitat, in acres or hectares. If you need, refer to Lab 9 near the end of part 2 for summarizing statistics of polygons.

Produce a map that includes the prime habitat, roads, streams, and topographic DRG background.  Include a descriptive legend that explains the process and the total size and units (acres or hectares), of potential grouse habitat in a text box, or in the legend.

You may want to use a transparent fill for the habitat polygons to improve the appearance of the map.

Also include the usual 1) title, including a description of the map and your name, 2) north arrow, 3)

- scale bar, and 4) a

complete, descriptive legend (no odd or filename labels).

Export a pdf or print this final map.

Here is an example of the general appearance of the final output map.

| Vegetation Codes: |  |  |
| --- | --- | --- |
| For the vegetation layer of cloquet_vegetation.shp |
| C_TYPE Species | SIZE_CL Size class |
| R | Red pine | a | Seedlings (0-1") |
| W | White pine | b | Saplings (1-5") |
| J | Jack pine | c | Poles (5-9") |
| A | Aspen | d | Small saw timber (9-14") |
| D | Scotch pine |  |  |
| WS | White spruce | DENS_CL Density class |
| S | Black spruce | I (1) | Poor (10-40% crown closure) |
| B | Birch | II (2) | Medium (40-70% crown closure) |
| C | White cedar | III (3) | Good (over 70% crown closure) |
| F | Balsam fir |  |  |
| T | Tamarack |  |  |
| Q | Mixed swamp conifers |  |  |
| E | Swamp - bottomlands, hardwood |  |  |
| U | Swamp - upland, brush |  |  |
| L | Lowland brush |  |  |
| G | Grassland |  |  |
| M | Marsh |  |  |
| SX | Non-productive |  |  |
| CO | Recent cutover |  |  |
| PX | Experimental planting |  |  |
| O | Open |  |  |